## Slide 1: Intro to PVC
Notes: If they have ever worked with PVC? What kinds of projects they’ve made with PVC? If they know what PVC is or made out of?”

## Slide 2: Objectives for today
Learn the different uses of PVC for industrial purposes and DIY uses
Learn how to prime and glue PVC together
Will be able to identify rigid and flexible PVC, elbows and tees
Will be able to design a PVC Sling Shots

## Slide 3: What is PVC?
PVC is short for Polyvinyl Chloride – a white, brittle solid
Third-most produced synthetic plastic in the world
Lightweight, durable, low-cost and easy installation
Two basic forms: Rigid and flexible
Used for pipes, medical devices, wire and cable insulation etc.!
Notes: 40 million tons of PVC produced each year

## Slide 4: Rigid PVC
Pros
Very stiff
Low cost
Good electrical insulation
Intrinsic flame retardant
Stability at room temperature
Cons
Difficult to melt
Becomes brittle at 41 degrees F
Used in construction for pipe and in profile applications such as doors and windows. It is also used in making bottles, non-food packaging, food-covering sheets and credit cards.

## Slide 5: Flexible PVC
Pros
Flexible
Low cost
High impact strength
Non-flammable
Good resistance to UV, acids and other inorganic chemicals
Cons
Can degrade in high temperatures
Lower chemical resistance than rigid PVC
Used in plumbing, electrical cable insulation, imitation leather, hoses and flooring.

## Slide 7: Elbows and tee’s
Notes: Coupling, cap, plug, male and female adapters

## Slide 8: Primer and glue
No ordinary glue, it’s a chemical solvent
Melts the surface of the PVC, quickly re-hardens which causes the PVC pieces to fuse together
Can be quite a tricky process!
Primer is used to clean and prep the PVC
Glue is used to create an airtight, leak-proof bond
Wait 10 seconds then you apply glue
Immediately attach your PVC together!
Hold in place and give a little twist before it sets

## Slide 9: Safety first!
Always wear safety glasses when priming and gluing PVC
Be aware of your workspace and clothing
Primer will stain whatever you get it on PERMINATLY
Keep both primer and flue away from any protentional sparks or flames
Avoid breathing in fumes from the glue
Do not get glue on your hands, eyes, hair, your friends or clothing
Make sure you have the correct kind of primer and glue
Notes: Matt Teague story

## Slide 10: Kahoot!
https://create.kahoot.it/details/3f2efa6b-959e-4afd-ad97-5d79ecf2193a